## Slide 1: Speed Management Study
September 2024

## Slide 2: Why Conduct a Speed Management Study?
Advance VZAP Policy Action 1.3
Improve human behavior and manage speeding
Accountability - Speeding & aggressive driving accounted for 17% of traffic-related deaths from 2017 to 2023

## Slide 3: Study Scope and Timeline
Identify appropriate Target Speeds and countermeasures
Uses national best practices and guidance for speed setting
Applies a Safe System approach to prioritize vulnerable road users
April 2024
May 2024
July 2024
September 2024
Study Kickoff
June 2024
August 2024
FDOT Coordination
Draft Target Speed Methodology
Estimated Completion
Final Target Speed Methodology
Operating Speed Data
Study Kickoff
FDOT Coordination
Draft Target Speed Methodology
Operating Speed Data
Final Target Speed Methodology
Estimated Completion
April
May
June
July
August
September
2024

## Slide 4: Speed Definitions
Design Speed
Target Speed
Posted Speed
Operating Speed
Notes: Target Speed is the highest speed vehicles should operate on a roadway, given the context of the roadway and consideration for multimodal users
Design Speed is the speed that regulates the roadway design including characteristics such as lane widths, clear zone, speeds, etc.
Posted Speed established by methods described in the Speed Zoning for Highways, Roads, and Streets in Florida Manual. This manual is adopted by Rule 14- 15.012, F.A.C. Generally set based upon doing a speed study and looking at the 85th percentile speed
Operating Speed - the speed at which drivers are observed traveling during free flow conditions. Generally considered the 85th percentile speed

## Slide 5: Target Speed Methodology
Data driven, point-based approach
Applied on…
  All Federal-Aid Roads not a State Road
  State, County, and Municipal roads on the TPA High Injury Network
Emphasizes most vulnerable roadway users
Roadway Characteristics
Safety Data
Multimodal Data
Geometric Data
Notes: Assigned Target Speed Range
Roadway Centerlines
Functional Classification
Roadway Ownership
FDOT D4 Context Classification
Safety Data
Palm Beach TPA HIN
FDOT VRU
Transit Data
Palm Tran Stop Level Transit Ridership
Geometric Data
Number of Lanes
Pedestrian and Bicycle Data
Palm Beach TPA LTS
Replica Origin Destination Data
The data was developed into a points-based methodology

## Slide 6: Draft Target Speed Results
Chart: Draft Target Speed Distribution
| 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
Non-SHS Arterial | 3.2304 | 59.8911 | 92.1158 | 33.0346 | 40.7869 | 22.1713 | 3.5865 | 13.4091
Non-SHS Collector | 0.52283 | 4.3374 | 77.4666 | 191.7995 | 107.0283 | 75.2965 | 56.6252
Local | 0.53629 | 12.7997 | 11.7597 | 2.4543 | 0.17543 | 1.0581
SHS (on the HIN only) | 2.1629 | 80.1481 | 50.9376 | 9.9599 | 0.074691 | 0.18965 | 0.35367
DRAFT
Notes: More than a third (~192 miles) of non- SHS collectors were assigned a 30 MPH target speed.
About a third (~92 miles) of non-SHS arterial roadways also have a 30 MPH target speed,
Local roads (~29 miles) and SHS roads (~144 miles), with SHS roads receiving the lowest target speeds (25 or 30 MPH)

## Slide 7: Draft Speed Comparative Analysis
Operating Speed Data
  85th Speed
  Median Speed
  Average Speed
Study Network Analysis
High Injury Network Analysis
vs.
vs.
Target Speed
Posted Speed
Posted Speed
Operating Speed
Notes: Operating Speed Data
RITIS
TMC codes from RITIS were added to the HIN network.
  The network was divided into positive (northbound/eastbound) and negative (southbound/westbound) TMC codes based on road direction.
  Some TMC codes required segmentation to align the linework with RITIS data, ensuring correct TMC representation.
TMC code data was downloaded from RITIS for speed analysis at the 85th, 50th, and Mean Speed intervals during the following periods:
  Weekday
  Weekend
  Overnight
TMC data was joined to the TMC code on the HIN network to conduct a Speed Comparative Analysis.
Conducted multiple different types of analyses with the operating speed data and on the study network.
We compared the Target Speed to the posted speed to identify locations with large differences to potentially prioritize.
For the HIN, conducted an operating speed analyses to identify location with potentially existing speeding concerns.

## Slide 8: Draft Priority Speed Management Corridors
Identification
Speeding
Traditionally Underserved Index
Posted Speed vs. Target Speed
Target Speed points
>
vs.
Posted Speed
Operating Speed
Posted Speed
Target Speed
Notes: To identify the high priority corridors, the following variables were considered. Corridors with existing speeding, traditionally underserved index (low income, racial %, English, disability, youth, elderly, 0 car HH).
Looking at locations with posted speed vs. target speed.
Overall Target Speed Points.

## Slide 9: Next Steps
Finalize priority speed management corridors
Identify countermeasures and strategies to achieve Target Speed
Complete Final Report
Median
Pinchpoint
Chicane
Lane Shift
Speed Hump
Roundabout
On Street Parking
Example Target Speed Countermeasures from NACTO

## Slide 10: Questions?

## Slide 11: Additional Information: Draft Operating Speed
Operating Speed Data
  85th Speed
  Median Speed
  Average Speed
Time Periods
  Weekday
  Weekend
  Overnight
Notes: Operating Speed Data
RITIS
TMC codes from RITIS were added to the HIN network.
  The network was divided into positive (northbound/eastbound) and negative (southbound/westbound) TMC codes based on road direction.
  Some TMC codes required segmentation to align the linework with RITIS data, ensuring correct TMC representation.
TMC code data was downloaded from RITIS for speed analysis at the 85th, 50th, and Mean Speed intervals during the following periods:
  Weekday
  Weekend
  Overnight
TMC data was joined to the TMC code on the HIN network to conduct a Speed Comparative Analysis.
Conducted multiple different types of analyses

## Slide 12: Additional Information: Draft Comparative Speed Analysis
Identification
Speeding
>
Posted Speed
Operating Speed